## Slide 1: Socket Communication using AT Commands
Assignment 6 - Cavli Module TCP Communication
Prepared by Abel Joy

## Slide 2: Why Socket Communication?
Required for IoT devices to communicate over the internet
Enables data exchange with cloud servers
Uses TCP/UDP over cellular networks
Common use cases:
- Remote server connection (e.g., MQTT/HTTP)
- Sending sensor data
- Receiving commands

## Slide 3: CelerSMS Limitation
CelerSMS AT Emulator only supports GSM SMS commands
Does NOT support socket commands like AT+QIOPEN or AT+QISEND
Real modem is required to test TCP socket flow

## Slide 4: Steps for TCP Socket Communication
1. Configure PDP context using AT+CGDCONT
2. Open socket using AT+QIOPEN
3. Send data using AT+QISEND
4. Receive response (if applicable)
5. Close connection using AT+QICLOSE

## Slide 5: AT+CGDCONT – Define PDP Context
Syntax:
AT+CGDCONT=<cid>,"<PDP_type>","<APN>"
• <cid>: Context ID (e.g., 1)
• <PDP_type>: Usually "IP"
• <APN>: SIM/network APN (e.g., "internet")
Example:
AT+CGDCONT=1,"IP","internet"

## Slide 6: AT+QIOPEN – Open TCP/UDP Socket
Syntax:
AT+QIOPEN=<ctxid>,<connectID>,"<service_type>","<ip>",<port>,<local_port>,<access_mode>
Example:
AT+QIOPEN=1,0,"TCP","142.250.196.78",80,0,0
Response:
OK
+QIOPEN: 0,0

## Slide 7: AT+QISEND – Send Data
Syntax:
AT+QISEND=<connectID>,<length>
After command, wait for ">" prompt
Type message and press Ctrl+Z
Example:
AT+QISEND=0,18
> Hello from Abel
Response:
SEND OK

## Slide 8: AT+QICLOSE – Close Socket
Syntax:
AT+QICLOSE=<connectID>
<connectID>: The socket ID to close
Example:
AT+QICLOSE=0
Response:
OK

## Slide 9: Sample Communication Flow
AT+CGDCONT=1,"IP","internet"
AT+QIOPEN=1,0,"TCP","142.250.196.78",80,0,0
+QIOPEN: 0,0
AT+QISEND=0,18
> Hello from Abel
SEND OK
AT+QICLOSE=0

## Slide 10: Conclusion
Socket communication allows TCP/UDP communication over cellular
IoT modules support it via AT+QIOPEN, AT+QISEND, AT+QICLOSE
Not testable on CelerSMS — needs real hardware
Useful for IoT applications (sensors, telemetry, remote control)